PRODUCT:  Manual Architectural-CM clutch roller shade with optional 5.5” fascia and bottom closure panel.  A premium clutch system engineered and designed for the most demanding applications.  The CM clutch provides smooth, quiet operation across a wide range of shade sizes.  The optional 5.5” bracket and fascia system are designed for tall shades where additional space is required for the large fabric roll and tube.  Options such as multi-band coupling, indexing, spring assist, and adjustable leveling brackets make this the most versatile shade system in the BlueShade product line.

PART 1 GENERAL

  - SECTION INCLUDES

    - Manual roll-up fabric interior window shades including aluminum fascia and mounting hardware to conceal shade hardware.

  - RELATED SECTIONS

    - Section 06 10 00 - Rough Carpentry.

    - Section 07 90 00 - Joint Protection.

    - Section 09 21 16 - Gypsum Board Shaft Wall Assemblies.

    - Section 09 51 23 - Acoustical Tile Ceilings.

  - REFERENCES

    - NFPA 701-99 - Fire Tests for Flame-Resistant Textiles and Films.

    - GREENGUARD Environmental Institute Children & Schools

    - US Green Building Council.

  - SUBMITTALS

    - Submit under provisions of Section 01 33 26 - Source Quality Control Reporting:

    - Product Data:  Manufacturer's data sheets on each product specified, including:

- Preparation instructions and recommendations.

- Installation and maintenance instructions.

- Styles, material descriptions, dimensions of individual components, profiles, features, finishes and operating instructions.

- Storage and handling requirements and recommendations.

- Mounting details and installation methods, including integration of hardware with building structure.

    - Shop Drawings:  Plans, elevations, sections, product details, installation details, operational clearances, and relationship to adjacent work.

    - Window Treatment Schedule:  For all roller shades.  Use same room designations as indicated on the Drawings, field verified window dimensions, quantities, type of shade, controls, fabric, and color, and include opening sizes and key to typical mounting details.

    - Selection Samples:  For each finish product specified, two complete sets of shade cloth options and aluminum finish color samples representing manufacturer's full range of available colors and patterns.

    - Verification Samples:  For each finish product specified, two complete sets of shade components, unassembled, demonstrating compliance with specified requirements.  Shade fabric sample and aluminum finish sample as selected, representing actual product, color, and patterns.  Mark face of material to indicate interior faces.

    - Maintenance Data:  Methods for maintaining roller shades, precautions regarding cleaning materials and methods, instructions for operating hardware and controls.

    - Manufacturer's Certificates: Certify products meet or exceed specified requirements.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Obtain roller shades through one source from a single manufacturer with a minimum of twenty years’ experience in manufacturing products comparable to those specified in this section.

    - NFPA Flame-Test: Passes NFPA 701. Materials tested shall be identical to products proposed for use.

    - Mock-Up:  Provide a mock-up of one of each type roller shade assembly specified for evaluation of mounting, appearance and accessories.

- Locate mock-up in window(s) designated by Architect.

- Do not proceed with remaining work until mock-up is accepted by Architect.

  - DELIVERY, STORAGE, AND HANDLING

    - Do not deliver window shades until building is enclosed and construction within spaces where shades will be installed is substantially complete.

    - Deliver products in manufacturer's original, unopened, undamaged containers with labels intact.

    - Label containers and shades according to Window Shade Schedule.

    - Store products in manufacturer's unopened packaging until ready for installation.

  - SEQUENCING

    - Ensure that locating templates and other information required for installation of products of this section are furnished to affected trades in time to prevent interruption of construction progress.

    - Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

  - PROJECT CONDITIONS

    - Install roller shades after finish work and ambient temperature, humidity and ventilation conditions are maintained at levels recommended for project upon completion.

  - WARRANTY

    - Initial warranty:  Provide an initial one-year warranty on all products and services, including installations, to be free from defects. Products or services found to be defective under normal use during this initial warranty period will be repaired or replaced without charge to the customer.  Refer to Blueshade® “Best-in-the-Business” warranty and exclusions.  Warranty period shall begin upon completion of the installation.

    - Extended Warranty: Provide a 25-year limited warranty. Refer to BlueShade® “Best-in-the-Business” warranty and exclusions.

PART 2 PRODUCTS

  - MANUFACTURERS

    - Basis of design: Blueshade by Drapery Industries Inc., Rochester, NY 14610,                       Toll free (844-737-2533), Web: www.blueshade.us.com

Product: Manual Architectural-CM premium clutch roller shade with 5.5” fascia and bottom closure panel.

    - Substitutions: Not permitted.

  - MANUAL WINDOW SHADES

    - Manually operated vertical roll-up shade with fabric, premium clutch, chain, fascia panel, and necessary hardware to complete installation.  BlueShade manual Architectural-CM series as manufactured by Drapery Industries Inc.

- Operation:  Bead chain and Galaxy-clutch operating mechanism, allowing heavy shades to be operated with reduced pull force.   Designed for mid-size shades where weight and tube deflection are an issue.  Clutch never needs adjustment or lubrication. Provide limit stops to prevent shade from being raised or lowered too far.

  - CM Clutch: Premium mechanical clutch designed for smooth, durable operation over a wide variety of shade sizes and weights. Bi-directional clutch fabricated from POM thermoplastic, comprised of PA6 with glass fiber, and steel spring; Molded chain placement guides allow the chain to drop behind the fascia, eliminating the need to notch the fascia panel.  Chain placement right or left.  White & Black color as selected by Architect.

  - Bead chain loop: Stainless steel bead chain hanging at side of window.

  - Bead Chain Hold Down: Spring-Loaded Tensioner (P-clip style without tensioner spring is not acceptable). Color as selected by Architect in Gray, White, Vanilla, Bronze or Black.

  - Idler Assembly: Provide heavy-duty idler assembly consisting of retractable pin end with metal gear for positive placement, and level adjusting idler bracket.  Idler pin designed with retractable geared pin-end to facilitate easy installation, and removal of shade for service.  Level adjusting idle end bracket consist of cold rolled steel bracket which is zinc plated and mechanically fastened to a plate assembly made from Acrylonitrile-Butadiene-Styrene (ABS) which is a polymerized alloy.  ABS is used when high impact resistance and a nice surface finish are desired.  Idler and adapter assembly designed for 1.75” diameter (OD) keyed tube.

- Roller tube: Keyed tube with a minimum 1.75” diameter (OD) fabricated from extruded aluminum, steel is not acceptable. Diameter, wall thickness, and material selected by manufacturer to accommodate shade size with minimum deflection.  Keyed tube design, reduces deflection over wide spans, and the key groove can accept optional fabric spline.  Standard fabric Connection to roller tube with LSE (low surface energy) double sided adhesive specifically developed to attach coated textiles to metal.  Welded fabric spline (optional).

- Mounting:  mounting brackets fabricated from cold rolled steel ASTM A1008, with zinc-plated finish. Size to be 5.5” deep x 5.5” high x 0.09” thick.

- Endcaps:  optional endcaps made from Acrylonitrile-Butadiene-Styrene (ABS) which is a polymerized alloy.  ABS is used when high impact resistance and a nice surface finish are desired.    Use endcaps when the sides of the mounting brackets are visibly exposed.  Color Anodized, White, or Bronze as selected by Architect.

- Fascia:  Extruded 5.5” aluminum fascia panel with spring-lock clips designed to mechanically snap on to mounting hardware and does not require exposed fasteners.  Extrusion provides top and bottom grooved ledges.  The upper ledge is designed to hook over the top of the bracket, and the bottom ledge is engineered to accept a mating extruded bottom closure panel. Size to be 5.5 inches in height.  Fascia can be mounted continuously across two or more shade bands.  No notching is required.  Provide matching end cap for installations where the sides of the mounting hardware are visible. Powder coat finish in color Anodized, White, or Bronze as selected by Architect.

- Bottom closure:  Extruded aluminum bottom closure panel designed to mate to 5.5” aluminum fascia panel.  Size available in 2” or 3” return, which shall be determined based on the diameter size of roller tube and fabric.  Powder coat finish in color Anodized, White, or Bronze as selected by Architect.

    - Fabric Length: Provide a minimum of 12" greater than window height.

    - Shade slat: Aluminum slat 1/8” x 1” MF encased in welded heat seamed hem.

    - Orientation: Regular (from back of roller).

  - FABRIC

    - Color and pattern:  __________, No. _____.

    - Color and pattern: As indicated in Color Schedule on Drawings.

    - Color and pattern: As selected by Architect from manufacturer's full range.

PART 3 EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of another sub-contractor, notify Architect of unsatisfactory preparation before proceeding.

  - PREPARATION

    - Coordinate requirements for blocking and structural supports to ensure adequate means for installation of pocket enclosure brackets, and hardware for installation of manual window shades.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions.

    - Install roller shades level, plumb, square, and true.  Allow proper clearances for window operation hardware.

    - Install after interior construction is essentially complete.

    - Remove and properly dispose of all debris and metal shavings.  Vacuum as necessary.

  - TESTING AND DEMONSTRATION

    - Test window shades to verify that controls, limit stops, interface to other building materials, and other operating components are functional. Correct deficiencies.

    - Demonstrate operation of shades to Owner's designated representatives.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

  - SCHEDULES

    - Refer to Drawings for shade types and locations.

END OF SECTION

# Text boxes

Specifiers: for more information

please contact us at:

www.blueshade.us.com

Toll Free: 844-737-2533